金桔果汁濃縮加工

李穎宏、陳正敏

四季桔原汁經連續離心(126,000rpm)所分離之油渣約佔10％，本試驗利用去油渣之四季桔汁分別進行薄膜濃縮結果：四季桔汁經連續離心後，分別以PCI AFC99在50Bar進行20℃及30℃濃縮。起始濃度為7.5。Brix，起始透流量分別為30.3 L/M2/H及40 L/M2/H，最終VCR分別達3.0及3.6，平均透流量分別為17.8 L/M2/H及20.1 L/M2/H，2種操作條件之最終滯流液濃度分別達17.4。Brix 及20.6。Brix(酸度分別為12.94％及13.69％)，且透流液皆無固形物檢出。若欲全數回添精油則汁液濃縮至少需達3.9倍濃縮。四季桔利用薄膜濃縮之模式與檸檬汁相類似。

表1.四季桔汁不同處理之濃縮過程品質比較

| Processing | TSSC | pH | Acidity |  | Color |  | Vicosity |
| --- | --- | --- | --- | --- | --- | --- | --- |
|  | (。Brix) |  | (％) | L | a | b | (cp) |
| fresh juice | 7.5 | 2.90 | 5.40 | 5.08 | 0.37 | 3.46 | 0.97 |
| Afc | 7.6 | 2.48 | 5.47 | 7.93 | 0.60 | 4.51 | 0.77 |
| Afu | 7.0 | 2.80 | 5.30 | 97.91 | -1.58 | 7.53 | 0.65 |
| AfcC20℃ | 17.4 | 2.34 | 11.94 | 4.68 | 1.01 | 3.14 | 0.95 |
| AfcC30℃ | 20.6 | 2.29 | 13.69 | 4.88 | 2.16 | 3.35 | 1.11 |
| AfuC30℃ | 21.7 | 2.22 | 15.24 | 93.75 | -3.94 | 23.54 | 0.85 |
| ReAfcC20℃ | 7.5 | 2.84 | 5.82 | 9.85 | 4.25 | 5.86 | 0.70 |
| ReAfcC30℃ | 7.4 | 2.44 | 5.13 | 16.11 | 8.21 | 10.03 | 0.73 |
| ReAfuC30℃ | 7.5 | 2.84 | 5.40 | 97.5 | -2.00 | 9.57 | 0.64 |
| UF retentate | 9.7 | 2.45 | 5.60 | 1.44 | 0.75 | 1.01 | 1.73 |

Afc: juice after continue centrifugation at 12600rpm, AfcC20℃:Afc juice concentrated with RO at 20℃,50bar, AfcC30℃:Afc juice concentrated with RO at 30℃,50bar, ReAfcC20℃: juice of AfcC20℃were reconstituted to the level of Afc, ReAfcC30℃: juice of AfcC20℃were reconstituted to the level of Afc, Afu: juice after ultra filtration at 8Bar, 30℃(UF permeate), AFuC30℃: UF permeate concentrated with RO at 30℃,50bar, ReAfuC30℃: juice of AfuC30℃were reconstituted to the level of Afu.

TSSC: Total soluble solid contents

# Text boxes

圖1.離心後四季桔汁在50bar壓力下20℃及

30℃之RO濃縮比較

圖2.四季桔汁離心液及UF透流液在50bar,

30℃之RO濃縮比較