蓮霧遮蔭時間長短對早花率的影響

李銘全、林娟如、林順臺

本研究於蓮霧催花前30～60天分期進行遮蔭處理，探討遮蔭時間之長短對早花率的影響，以期後續開花數量符合農民預期，避免日後疏花、疏果等繁瑣之人工作業，節省經營成本。由於高屏地區7～9月為連續降雨氣候，適值遮蔭處理時期，及低日照之環境，測定蓮霧遮蔭後樹冠下之光合作用光子流密度(Photosynthesis photon flux density, PPFD)，調查結果發現方位不影響其數值，但隨遮蔭處理時間的增長，其PPFD逐漸下降，以遮蔭處理30天者之13.86μmol/m2/s為最高，50天之5.23μmol/m2/s為最低。花穗因著生方位不同而有所區別，但僅50天遮蔭處理達顯著差異，其餘處理組則無顯著差異。經由60、50、40及30天遮蔭處理其平均單株花穗數分別為1067、1031、949及961個，以60天處理平均單株1067個花穗為最多，40天處理組之949個為最低。光合作用光質流密度與花穗數之相關性甚低，其迴歸方程式為y＝-11.359X＋1098.5，相關系數R2＝0.045。果實成熟期受到冬季寒害之影響，果實掉落嚴重，以致無法分析遮蔭處理與產量之關係。

表一、不同遮蔭天數對蓮霧光合作用光子流密度之影響

Tab.1. The effects of different shading time on the PPFD of wax-apple.

|  | 60 Days | 50 Days | 40 Days | 30 Days |
| --- | --- | --- | --- | --- |
| PPFD | 5.98 c | 5.23 c | 9.01 b | 13.86 a |

Values within the column followed by different letter are significantly different (P＜0.05) by Duncan’s multiple range test.

表二、不同遮蔭天數對東、西、南、北向蓮霧花穗數之影響

Tab.2. The spikelet numbers in different direction of wax-apple in different shading time.

| Spikelet Direction | 60 Days | 50 Days | 40 Days | 30 Days |
| --- | --- | --- | --- | --- |
| East | 287 a | 249 ab | 228 a | 254 a |
| West | 279 a | 291 a | 204 a | 269 a |
| South | 236 a | 231 b | 231 a | 189 a |
| North | 265 a | 231 b | 281 a | 249 a |

Values within the column followed by different letter are significantly different (P＜0.05) by Duncan’s multiple range test.

圖一、蓮霧遮蔭光合作用光質流密度與平均單株花穗數之相關

# Fig.1. The correlation between the spikelet numbers per-plant and PPFD.